## Slide 1
B.TECH CAPSTONE PROJECT
VI Semester | 2023–2027
AI-Based
Multi-Plant
Defect Detection
& Process Risk
Prediction
in Potato Chip Manufacturing
using CNN and Random Forest
Team 29
Guide: Dr. Sankar K | Dept. of CSE (AI/ML)
Jain (Deemed-to-be University), Bengaluru
Project Highlights
93.87%
CNN Test Accuracy
MobileNetV2 Transfer Learning
R² = 0.912
Random Forest R² Score
Process Risk Prediction
₹45.27L
Projected Annual Savings
Per plant COPQ reduction
Raj Mehta · Priyanshu Soni · Karthik Khandka · Yuvraj Joshi · Shreyas Singh

## Slide 2
PROBLEM
Why Manual Quality Control Fails
Human Fatigue & Inconsistency
Inspectors miss 15–20% of defects at high throughput. Inspector-to-inspector variability means results are never standardized.
No Predictive Capability
Inspection is entirely reactive — there is no mechanism to anticipate defects from fryer process conditions before they occur.
Disconnected from Root Cause
Observed defects are not linked to upstream fryer parameters, making root cause analysis slow and remediation guesswork.
Multi-Plant Blindspot
Large manufacturers have no standardized KPI benchmarking across facilities, preventing best practices from being identified.

## Slide 3
ARCHITECTURE
5-Layer Modular System Design
1
Input Layer
OpenCV · Pandas
Chip images (camera feed) + Fryer sensor data (process parameters)
2
Preprocessing Layer
Keras ImageDataGenerator · NumPy
Resize 224×224 · Normalize · Augment images | StandardScaler for features
3
Model Layer
TensorFlow/Keras · scikit-learn
CNN (MobileNetV2) → Defect Classification | Random Forest → Defect % Prediction
4
Analytics Layer
SHAP · SciPy · Pandas
SHAP Explainability · ANOVA + Pearson Correlation · Cost Impact Model
5
Presentation Layer
Streamlit · Plotly · Matplotlib
Streamlit Dashboard — Defect Detection Tab | Risk Predictor Tab | Benchmarking Tab

## Slide 4
MODEL 1 — CNN
MobileNetV2 Transfer Learning — Defect Detection
Input
224×224
MobileNetV2
Base
GlobalAvg
Pool2D
Dense
128+ReLU
Dropout
0.5
Sigmoid
Output
Two-Phase Training Protocol
Phase 1 — Feature Extraction
Freeze entire MobileNetV2 base
Train classification head only | LR = 1×10⁻³ | 10 epochs
Phase 2 — Fine-Tuning
Unfreeze top 30 MobileNetV2 layers
Full model training | LR = 1×10⁻⁵ | 10 epochs + ReduceLROnPlateau
Test Set Performance
93.87%
Accuracy
0.930
F1-Score
0.978
AUC-ROC
47 ms
Inference

## Slide 5
MODEL 2 — RF
Random Forest Regression — Process Risk Predictor
Feature Importance (MDI)
Fryer Temperature
34.2%
Oil Quality Index
28.1%
Moisture Content
18.4%
Frying Time
12.4%
Slice Thickness
6.9%
Model Performance on Test Set
R² Score
0.912
Excellent fit — 91.2% variance explained
MAE
1.42%
Within ±2% manual defect count uncertainty
RMSE
2.07%
Higher than MAE — occasional extremes
CV R²
0.898 ± 0.023
Stable across 5 folds — robust model
Best Hyperparameters (GridSearchCV 5-fold): n_estimators = 200 · max_depth = 20 · min_samples_split = 5 · max_features = sqrt

## Slide 6
VALIDATION
SHAP Explainability & Statistical Validation
SHAP Explainability
TreeExplainer for RF — exact SHAP values (game theory basis)
GradientExplainer for CNN — pixel-level saliency maps
fryer_temperature shows widest SHAP value spread
Burnt chips: heatmap highlights darkened regions
Waterfall charts: per-prediction feature breakdown
SHAP overlay available in Streamlit dashboard
ANOVA Results (all p < 0.001)
Parameter
F-Statistic
Pearson r
Fryer Temperature
287.43
0.82
Oil Quality Index
219.61
0.73
Moisture Content
143.28
0.61
Frying Time
87.55
0.48
Slice Thickness
34.17
0.31
All 5 parameters statistically significant · Consistent with RF feature importance rankings

## Slide 7
DASHBOARD
Streamlit Dashboard — Three Interactive Tabs
01
Tab 01: Defect Detection
Drag-and-drop JPEG/PNG chip image upload · MobileNetV2 inference → DEFECTIVE / NON-DEFECTIVE · Confidence % with color-coded badge (green/amber/red) · Optional SHAP pixel saliency heatmap overlay on image · Session prediction log exportable as CSV
02
Tab 02: Process Risk Predictor
5 interactive sliders (temp · frying time · moisture · thickness · oil TPM) · Real-time RF prediction updates without page reload · Plotly circular gauge vs industry thresholds · SHAP waterfall chart for current parameter set · Risk tiers: Low < 5% · Medium 5–12% · High > 12%
03
Tab 03: Multi-Plant Benchmarking
Side-by-side bar chart: avg defect rate across plants · 12-month weekly defect rate trend lines per facility · Composite quality score ranking table (out of 100) · Defect type heatmap per plant for targeted intervention · Plant C: 91 · Plant A: 82 · Plant B: 54 (out of 100)

## Slide 8
RESULTS
Performance Comparison & Financial Impact
System Comparison
System
Accuracy
Throughput
Predictive?
Annual COPQ
Manual Inspection
78–82%
50–80/min
No
₹77.68L
Rule-Based Vision
85–88%
200/min
No
₹55.40L
Our AI System (CNN + RF)
93.87%
1,200/min
Yes
₹32.41L
Projected Annual COPQ Savings per Plant
₹18.67L
Defect Disposal
₹5.62L
Rework Costs
₹10.92L
Inspector Labor
₹4.88L
Complaints
Total Annual Saving: ₹45.27 Lakhs / plant · Estimated Payback Period: 2–3 months

## Slide 9
CONCLUSIONS
Key Conclusions & Future Scope
Conclusions
CNN (MobileNetV2): 93.87% accuracy, 7.7% miss rate vs 15–20% manual
RF Regressor: R²=0.912, MAE=1.42% — strong process prediction
ANOVA confirms all 5 parameters significant (p<0.001)
SHAP makes predictions interpretable to non-ML engineers
₹45.27L annual COPQ savings per plant, 2–3 month payback
Integrated reactive + proactive quality system in one dashboard
Future Scope
Real-Time Video:
30fps GPU inference on live conveyor
Edge Deployment:
TFLite on NVIDIA Jetson / Raspberry Pi
Real Sensor Data:
PLC/SCADA pipeline for authentic fryer data
Multi-Class CNN:
Burnt · under-fried · broken · green · oil-patch
LSTM Temporal:
Capture process history for better prediction
Federated Learning:
Cross-plant model training without raw data sharing

## Slide 10
Thank You
Questions & Discussion Welcome
GitHub Repository
github.com/priyanshu812/potato-chip-ai-quality-monitor
Team 29 · Raj Mehta · Priyanshu Soni · Karthik Khandka · Yuvraj Joshi · Shreyas Singh
Guide: Dr. Sankar K · Dept. of CSE (AI/ML) · Jain (Deemed-to-be University)